## Slide 1
多核系统的缓存
陈志文
2017.12.13
E-mail: zhiwenchen@hnu.edu.cn
1
Notes: 1

## Slide 2
内 容
背景和基本概念
缓存的组织结构和工作原理
缓存一致性协议
缓存相关的性能问题
参考文献
2

## Slide 3: The Motivation for Mem Hierarchy
CPU Registers
100s Bytes
0.3-0.5 ns
L1 and L2 Cache
10s-100s K Bytes
~1 ns - ~10 ns
Main Memory
G Bytes
200ns ~ 300ns
~ $15/ GByte
Disk
1s -10s T Bytes
~ 10 ms
~ $0.15 / GByte
Capacity
Access Time
Cost
Registers
L1 Cache
Memory
Disk
Instr. Operands
Blocks
Pages
prog./compiler
4-8 bytes
cache cntl
32 or 64 bytes
OS
4K~ 64K bytes
Upper Level
L2 Cache
cache cntl
64 or 128 bytes
Blocks
Lower Level
faster
Larger
Trading off between capacity and latency
On Chip
Off Chip

## Slide 4: Processor and Memory are Far Apart
processor
memory
interconnect
Notes: From our point of view, one architectural principle drives everything else: processors and memory are far apart.

## Slide 5: Reading from Memory
address
Notes: It takes a long time for a processor to read a value from memory. It has to send the address to the memory …

## Slide 6: Reading from Memory
zzz…
Notes: Wait for the message to be delivered …

## Slide 7: Reading from Memory
value
Notes: And wait or the response to come back.

## Slide 8: Writing to Memory
address, value
Notes: Writing is similar, except you send the address and the new value, …

## Slide 9: Writing to Memory
zzz…
Notes: Wait …

## Slide 10: Writing to Memory
ack
Notes: And then get an acknowledgement that the new value was actually installed in the memory.

## Slide 11: Cache: Reading from Memory
address
cache
Notes: We alleviate this problem by introducing one or more caches: small, fast memories situated between main memory and processors.

## Slide 12: Cache: Reading from Memory
cache
Notes: Now, when a processor reads a value from memory, it stores the data in the cache before returning the data to the processor.

## Slide 13: Cache: Reading from Memory
cache
Notes: Later, if the processor wants to use the same data …

## Slide 14: Cache Hit
cache
?
Notes: When a processor wants to read a value, it first checks whether the data is present in the cache …

## Slide 15: Cache Hit
cache
Yes!
Notes: If so, it reads directly from the cache, saving a long round-trip to main memory. We call this a cache hit.

## Slide 16: Cache Miss
address
cache
?
No…
Notes: Sometimes the processor doesn’t find what it is lookin for in the cache.

## Slide 17: Cache Miss
cache
Notes: We call this a cache miss.

## Slide 18: Cache Miss
cache

## Slide 19
Background and Basic Concepts
What is cache?
  A smaller,faster memory that store a subset of a larger memory space
Why need cache?
  Bridge the speed gap between the fast processor and the slower memory
19
Notes: 19

## Slide 20
Programs’ Locality
Programs tend to exhibit temporal and spatial locality
Temporal locality: Once programs access data items or instructions they tend to access them again in the near future.
Spatial locality: Once programs access data items or instruction, they tend to access nearby data items or instruction in the near future.
20
Notes: 20

## Slide 21
Cache Line and Performance Metrics
When there is a cache miss, a fixed size block of consecutive data elements, or line, is copied from main memory to the cache.
Typical cache line size is 4-128 bytes.
Main memory can be seen as a sequence of lines, some of which can have a copy in the cache.
Cache Hit and Miss : When the data is found in the cache, we have a cache hit, otherwise it is a miss
21
Notes: 21

## Slide 22
Outline
背景和基本概念
缓存的组织结构和工作原理
缓存一致性协议
缓存相关的性能问题
参考文献
22

## Slide 23
Cache Organizations (Shared L2 Cache)
23
Notes: 23

## Slide 24
Workflow of Caches
Step 1:First check whether the line containing the address is currently stored in the L1 cache.
Step 2:If not in L1, the process repeats for the next level in the memory hierarchy,util the line is found.
Step 3:Use a cache replacement algorithm to replace the evicted line with the newly-retrieved line.
24

## Slide 25
缓存行替换策略
随机法；
先进先出法；
LRU法和LFU法；
自适应的替换策略
25
Notes: 25

## Slide 26
Write Policy for Flush
Write-through policy: A write to the cache causes a write to the main memory
Write-back policy: Writes to the main memory are delayed: cache lines that have been written over in the cache are marked dirty, and dirty cache lines are written to the main memory when they are evicted from the cache (following the replacement policy).
26
Notes: 写回法，是当cache写命中时，只修改cache的内容，不修改主存，只有当对应的缓存行被替换时才写回主存。
这种策略提供读写双向的高速缓存，并且减少访问主存的次数，提高效率。
缺点是造成cache-主存严重的不一致性。
写直达法，是当cache写命中时，cache与主存同时发生写修改，
这种策略较好的维护cache与主存的内容一致性。无需对cache行设置修改位和相应的测判逻辑，
缺点是cache对CPU向主存的写操作没有高速缓存功能，效率相对较低。
当发生写未命中时，直接写入主存，有两种不同策略，下一张内容介绍。
26

## Slide 27
Two Approaches for Write Miss
no-write-allocate policy: the cache line is not loaded into the cache, instead, the data is directly written into the main memory.
write-allocate policy: the cache line is loaded into the cache, then overwritten into the cache with the new data (write hit).
27
Notes: 当发生缓存未命中时，直接向主存写入。
根据是否将修改过的主存块取到cache有两种不同的策略：一是不取入，数据直接写入主存；
这种方法操作简单，但会降低命中率。
另一种是取入并分配一个缓存行。
较好的保持一致性，但操作复杂。
27

## Slide 28
Outline
背景和基本概念
缓存的组织结构和工作原理
缓存一致性协议
缓存相关的性能问题
参考文献
28

## Slide 29
Function of Cache-coherence Protocol
Maintain the consistency of data in the caches.
hardware threads typically rely on the cache-coherence protocol for communication.
Implements the two fundamental operations of an architecture: load (read) and store (write).
Communication between cores occurs implicitly as result of loads and stores.
29
Notes: 29

## Slide 30
MESI Protocol
MESI Protocol States
MESI协议状态迁移图
30
Notes: 30

## Slide 31
Drawbacks with MESI
Drawback 1: May send many high-latency messages that contain redundant data.
Drawback 2: The only way for data from a Modified cache line to be accessed by remote hardware threads is to flush data to the main memory and fetch it again.
31
Notes: 31

## Slide 32
Extended MESI Protocol
MESIF protocol: Used by Intel CPUs since the Nehalem
architecture. the extended forward state (a special form of the shared state) indicates the only cache that will respond to a load request for that line.
MOESI protocol: Used by AMD and Sun/Oracle CPUs. The extended owned state allows a core to load a modified line of another core without the need to invalidate the modified line.
GOLS protocol: Used by Xeon Phi. Use GOLS (Globally Owned Locally Shared) to simulate a Owned state, thus allowing the share of a modified line.
32
Notes: 32

## Slide 33
Techniques to Implement Coherence
Snoop based: All caches on the bus snoop the bus to determine if they have a copy of the block of data that is requested on the bus (e.g., source-based snooping and home-based snooping In Intel HasWell-EP Architecture).
Directory based: A directory keeps approximate or presise information of which caches hold copies of a memory location, When a cache line is changed the directory either updates or invalidates the other caches with that cache line to enforce coherence (e.g., AMD Opteron and Xeon Phi).
33
Notes: 之前提出的预取 都是采用 硬件预取的方式 ，对于随机访问模型是无效的， 需要数据结构的支持，比如说数组，对数组遍历的时候，直接访问元素的下一个位置即可，这是可以在硬件层面上实现。
但是对于随机访问的数据结构，比如hash，硬件层面就没法提供支持了，只能考程序员手动的通过代码提供支持。主要是通过设定PDIST这个值。
33

## Slide 34
Outline
Background and Basic Concepts
How Caches are Organized and Work
Cache-coherence Protocol
Cache Related Performance Issues
Reference
34

## Slide 35
Cache line ping-ponging or tennis effect
One processor writes to a cache line and then another processor writes to the same cache line but different data element
Cache line is in a separate socket/separate L2 cache environment
Each core would take a HITM (HIT Modified) on the cache line causing it to ship across the FSB (Front Side Bus to memory)
This increases the FSB traffic and even in good conditions costs about ½ the cost of a memory access
35
Notes: 35

## Slide 36: With a separated cache
CPU1
CPU2
Memory
Front Side Bus (FSB)
Cache Line
Shipping L2 Cache Line
~Half access to memory
Intel® Core™ Microarchitecture – Memory Sub-system
Notes: There is often an effect called ping-ponging or tennis where one processor writes to a cache line and then another processor writes to the same cache line but different data element
In a separate socket/separate last level cache environment
  Each core would take a HITM (HIT Modified) on the cache line causing it to ship across the FSB
  This increases the FSB traffic and even in good conditions costs about ½ the cost of a memory access

## Slide 37: Advantages of Shared Cache – using Advanced Smart Cache® Technology
CPU2
CPU1
Memory
Front Side Bus (FSB)
Cache Line
L2 is shared:
No need to ship cache
line
Intel® Core™ Microarchitecture – Memory Sub-system
Notes: Shared L2
No need to ship cache line
Cache line just goes from exclusive to shared for the other core to read.

## Slide 38: False Sharing
Performance issue in programs where cores may write to different memory addresses BUT in the same cache lines
Known as Ping-Ponging – Cache line is shipped between cores
Core 0
Core 1
Time
1
0
X[0] =
1
X[1] =
1
1
X[0] =
0
X[1] =
0
1
0
X[0] =
2
1
1
2
False Sharing not an issue in shared cache
It is an issue in separated cache
Notes: Intel book – Multi-core Programming – Increasing Performance Through Software Multi-threading by Shameem Akhter and Jason Roberts
False Sharing The smallest unit of memory that two processors interchange is a cache line or cache sector. Two separate caches can share a cache line when they both need to read it, but if the line is written in one cache, and read in another, it must be shipped between caches, even if the locations of interest are disjoint.
Like two people writing in different parts of a log book, the writes are independent, but unless the book can be ripped apart, the writers must pass the book back and forth. In the same way, two hardware threads writing to different locations contend for a cache sector to the point where it becomes a ping-pong game.
In this ping pong game, there are two threads, each running on a different core. Each thread increments a different location belonging to the same cache line. But because the locations belong to the same cache line, the cores must pass the sector back and forth across the memory bus.
In order to avoid false sharing – we need to alter either the algorithm or the data structure. We can add some “padding” to a data structure or arrays ( just enough padding generally less than cache line size) so that threads access data from different cache lines. Or we can adjust the implementation of the algorithm (the loop stride) to access data in different cache line for each thread

## Slide 39: Avoiding False Sharing
Algorithm
adjust the implementation of the algorithm (the loop stride) to access data in different cache line for each thread
Data Structure
add some “padding” to a data structure or arrays ( just enough padding generally less than cache line size) so that threads access data from different cache lines.
Profilers
DProf [10] are designed to locate cache locality bottlenecks, Sheriff [11] specifically detects false sharing and protects applications from it by adaptively isolating shared updates from different threads into separate physical addresses. LASER [12] which leverages new performance counter capabilities available on Intel’s Haswell architecture to detect and repair false sharing.

## Slide 40
Cache contention and pollution
Cache contention (especially in LLC): Caused by access contention in last level shared caches from multiple running threads.
Cache pollution: Happens when data sets with strong locality may not be allocated with sufficient cache space, access to the data with weaker locality may flush the to-be-reused data of its co-running applications from the shared LLC and significantly slow down these applications.
Solutions: ULCC [13], a software runtime library based on page-coloring technique for last level cache usage management, SRM-Buffer [14], a buffer cache design for multicore systems to address effectively the cache pollution problem caused by OS buffer
40
Notes: 40

## Slide 41
Outline
Background and Basic Concepts
How Caches are Organized and Work
Cache-coherence Protocol
Cache Related Performance Issues
Reference
41

## Slide 42
References
[1] Yarom Y, Ge Q, Liu F, et al. Mapping the Intel last-level cache[R]. Cryptology ePrint Archive, Report 2015/905, 2015.
[2] Irazoqui G, Eisenbarth T, Sunar B. Systematic reverse engineering of cache slice selection in Intel processors[C]//Digital System Design (DSD), 2015 Euromicro Conference on. IEEE, 2015: 629-636.
[3] Intel A. Introduction to the Intel QuickPath Interconnect[J]. White Paper, 2009.
[4] Molka D, Hackenberg D, Schone R, et al. Cache Coherence Protocol and Memory Performance of the Intel Haswell-EP Architecture[C]//Parallel Processing (ICPP), 2015 44th International Conference on. IEEE, 2015: 739-748.
42
Notes: 42

## Slide 43
References
[5] Lozi J P. Towards more scalable mutual exclusion for multicore architectures[D]. Université Pierre et Marie Curie-Paris VI, 2014.
[6]https://blogs.oracle.com/dave/entry/numa_aware_placement_of_communication1
[7] http://lackingrhoticity.blogspot.hk/2015/04/l3-cache-mapping-on-sandy-bridge-cpus.html
[8] http://blog.stuffedcow.net/2013/01/ivb-cache-replacement/
[9] Ramos S, Hoefler T. Modeling communication in cache-coherent SMP systems: a case-study with Xeon Phi[C]//Proceedings of the 22nd international symposium on High-performance parallel and distributed computing. ACM, 2013: 97-108.
43
Notes: 43

## Slide 44
References
[10] A. Pesterev, N. Zeldovich, and R. T. Morris. Locating cache performance bottlenecks using data profiling. In Proceedings of the 5th European Conference on Computer Systems,
EuroSys ’10, pages 335–348, New York, NY, USA, 2010. ACM.
[11] T. Liu and E. D. Berger. Sheriff: precise detection and automatic mitigation of false sharing. In Proceedings of the 2011 ACM International Conference on Object Oriented Programming Systems Languages and Applications, OOPSLA ’11, pages 3–18, New York, NY, USA, 2011. ACM.
[12] Luo L, Sriraman A, Fugate B, et al. LASER: Light, Accurate Sharing dEtection and Repair[J]. LASER, 2016, 3: 14-2016.
44
Notes: 44

## Slide 45
References
[13] Ding X, Wang K, Zhang X. ULCC: a user-level facility for optimizing shared cache performance on multicores[C]//Acm sigplan notices. ACM, 2011, 46(8): 103-112.
[14] Ding X, Wang K, Zhang X. SRM-buffer: an OS buffer management technique to prevent last level cache from thrashing in multicores[C]//Proceedings of the sixth conference on Computer systems. ACM, 2011: 243-256.
[15] David T, Guerraoui R, Trigonakis V. Everything you always wanted to know about synchronization but were afraid to ask[C]//Proceedings of the Twenty-Fourth ACM Symposium on Operating Systems Principles. ACM, 2013: 33-48.
[15] http://www.realworldtech.com/sandy-bridge/
[16] Qureshi M K, Jaleel A, Patt Y N, et al. Adaptive insertion policies for high performance caching[C]//ACM SIGARCH Computer Architecture News. ACM, 2007, 35(2): 381-391.
45
Notes: 45

## Slide 46
Thank You
46